## Slide 1: Multi Mode Same Band Contesting and Prep for Field Day Use
N6MDV K6VHY
June 18, 2018

## Slide 2: Why This Briefing?
It has been suggested we do more digital modes in 2018
  Field Day 2018 Digital Modes RTTY, PSK31, and FT8 are options
  We also want to do SSB and CW
  Digital modes are normally between x.070 and x.100 MHz
    Where X is the band frequency such as 7 or 14 for 40 and 20 meters
  CW modes are typically below x.070
  SSB/Voice is typically above x.125 or x.150
Why digital?
  Enables contacts on higher bands despite poor sunspot propagation
    Lower SNR required than phone contacts
  Develop additional skills for weak signal emergency communication
  Easier to learn than CW for weak signal use
  Possibly attract additional operators who don’t do CW or Phone
Multi mode would mean doing CW or Digital while also doing SSB
  Issue will be self interference by having more than one transmitter on the same band

## Slide 3: How to Avoid Self Interference local QRM
For the past few years we have had just one transmitter per band
  We use band pass filters from W3NQN on each transceiver
  With about 40dB on each filter gives us nearly 80dB separation between transceivers
  Hence no inter-station interference since we started using these filters
This works fine inter band, but not within a band

## Slide 4: Field Day Multi Mode Multi Band
The rules allow us to make a QSO with every station on
  Each band and each mode (CW, digital, voice)
  With the 10 HF/VHF/UHF bands this could be 30 contacts per other station
  A group on the east coast (MDC) actually runs a 27A setup
    3 modes times 9 of the bands
    They do it with good radios and careful placement of antennas
Good placement of antennas is physically separating the same band antennas
Good radios have good dynamic range, good filters, and low phase noise

## Slide 5: Our Suggested Approach
Run 3A plus GOTA and VHF stations
For the 3A part plan on:
  20M SSB/digital/CW
  15/80M SSB/digital/CW
  40M SSB/digital/CW
For the VHF plan on
  6M SSB, 2M FM, 440 FM (220 optional)
For GOTA plan on:
  GOTA coach for double points
  Work to get 20 contacts per new person
  Use 2M FM and 440FM
  Use 20M and possibly 40M SSB/digital
    New this year operate the voice while main stations are digital/CW
    Operate digital while main stations are voice

## Slide 6: Proper Spacing and Orientation two 3 Element Yagi
Antenna nulls at 90 degrees
  Roughly -34 to -24dBi
14dBi
12dBi
-10 –> 0 dBi
-24 dBi
3 element 55 ft
3 element 20 ft

## Slide 7
N
g
info
Park Entrance
pond
A – Antenna
g - generator
Info – Public Information Table
GOTA – Get on the Air Station
amphitheater
VHF cluster
TH3MK4
+ inverted V
A
A
A
pine
TH3jr
A
GOTA
70 degrees beam orientation
Optimum for East Coast and midwest
Northern states & midwest 30 deg
East coast late afternoon 15M 50 deg
Hawaii 260 deg
Alaska 330 deg
Antenna Placement
Magnetic Headings
Distances between stations
20M
40M

## Slide 8: Test Specs for Radios We Have Used in Past FD’s Green numbers are preferred for FD per Sherwood Engineering

## Slide 9: Definitions from http://www.sherweng.com/table.html Receiver evaluations
Phase noise is a significant problem in some cases: You have a neighboring ham close by, during Field Day when there are multiple transmitters at the same site, and certainly in a multi-multi contest station. You would like the number to be better that 130 dBc / Hz at 10 kHz.
Dynamic range is defined as the level in dB when two strong test signals make distortion in the radio equal to the noise floor. The radio thus can handle that range of signals before the strong signals just start to overload the radio.
What do you need in the way of close-in dynamic range? You want a number of at least 70 dB for SSB, and at least 80 dB for CW. A 10 dB safety factor would be nice, so that means you would prefer 80 dB for SSB and 90 dB for CW. Now there are several radios in the top ten that meet that specification.

## Slide 10: Summary
Try to have CW/Digital/SSB at all stations
For concurrent band sharing with GOTA
  Place antennas with nulls facing each other
  Use good radios
  Avoid excess power
  Schedule use as needed
(A rule – a transmitter can be used for only one call sign
  So unable to just declare one of the main machines as GOTA temporarily
  )

## Slide 11: Results Summary
Thoughts?

## Slide 12: Update After Field Day
We did install the two tri band antennas as shown
  Using the Kenwood TS930S on the 20M tower beam
  Using a KX3 with amplifier on 20M pushup pole at 20 feet GOTA
At 10W on the KX3 or 100W on the Kenwood
  Friday night, no visible S meter change or able to hear within 20KHz of each other
At 100W on both radios
  Saturday no visible S meter change or able to hear within 20KHz
  Later in the day as both stations search and pounced reportedly both could hear each other.
Conclusion
  This worked well. Do it again next year
  GOTA contact contact was higher this year as well